## Slide 1: EASA European Aviation Safety Agency
The common European civil aviation authority.
Cologne, Germany
Presentation CIA meeting March 2008
Updated March 25, 2008

## Slide 2: EASA founded upon EU directive in 2002
Basic: EC 1592/2002
  Replaced by EC 216/2008
Airworthiness: EC 1702/2003
Maintenance: EC 2042/2003
Regulations are approved by EU via the EU-Commission, the EU Council and the EU Parliament
        HÅ 2008-03-25

## Slide 3: REGULATION STRUCTURE
ER: Essential Requirements
IR: Implementing Rules
GM: Guidance Material
AMC: Acceptable Means of Compliance
CS: Certification Specifications
CS 30 Airships
CS 31 Balloons (HAB, GB, TGB, HAAS)

## Slide 4: PART M 2005
Airworthiness, maintenance, maintenance training and training organisation.
Covering rules for all aircraft
Based on rules for heavy commercial airliners
Met with strong opposition

## Slide 5: A-NPA 14-2006 ADVANCE NOTICE OF PROPOSED AMENDMENT.
(June 2006 - end of comments: 16 October 2006)
A concept for better regulation in General Aviation
(Aircraft other than Complex Motor Powered Aircraft, used in Non-commercial activities)

## Slide 6: Commercial activities:
"commercial operation"
shall mean any operation of an aircraft, in return for remuneration or other valuable consideration, which is available to the public or, when not made available to the public, which is performed under a contract between an operator and a customer, where the latter has no control over the operator;
(EC 216/2008, replacing EC1592/2002)
HÅ 2008-03-25

## Slide 7: The European Light Aircraft Process
To address the concerns in the area of initial airworthiness (design, certification and production) EASA proposes to introduce a simplified regulatory regime based around a new process for the
European Light Aircraft (ELA).

## Slide 8: ELA can be summarised as
ELA 1: Substantially simplified processes below 1000 kg. (Small balloons and simple airships)
ELA 2: Simplified processes below 2000 kg. (Larger balloons and airships other than transport airships)

## Slide 9: ELA 1 Aerostats
Maximum design lifting gas or hot air volume of not more than:
  3400 m3 for hot-air balloons
  1050 m3 for gas balloons
  300 m3 for tethered gas balloons
A non-complex airship designed for not more than two occupants and a maximum design lifting gas or hot-air volume of not more than:
  2500 m3 for hot-air airships
  1000 m3 for gas airships

## Slide 10: ELA 2
A non-complex aeroplane with MTOM less than 2000kg
A balloon
A hot-air airship
A gas airship meeting all the following elements:
  (i) 3% maximum static heaviness
  (ii) Non-vectored propulsion (except reverse thrust)
  (iii) Conventional and simple design of the:
    Structure
    Control system
    Ballonet system
  (iv) Non power-assisted controls

## Slide 11: NPA ELA
Initial airworthiness (design and maintenance)
Publication end of March 2008. Comments accepted until June.

## Slide 12: NPA No 2007-08
Revised Part-M requirements for aircraft not used in Commercial Air Transport
and
Pilot / owner maintenance
Published: 22 June-15 October 2007
Comments have been reviewed by EASA
HÅ 2008-03-30

## Slide 13: PILOT / OWNER MAINTENANCE TASKS for BALLOONS and AIRSHIPS
Specific basic principles for hot air airships, hot air balloons and gas balloons:
In addition to the basic principles, no task that is considered “complex” may be carried out by the pilot / owner of the balloon or hot air airship.
A complex task is considered as any maintenance or repair to the envelope or to the basket primary suspension system that requires the re-manufacture of any joint and/or component.
Any repair carried out to the envelope cannot include the repair or replacement of load tapes. Welding to the basket frame or burner frame or repairs to the pressure lines of the burners or the fuel cylinders are also prohibited.

## Slide 14: A) ENVELOPE (HAB)
1. Fabric repairs- excluding complete panels (as defined in, and in accordance with, Type Certificate holders' instructions) not requiring load tape repair or replacement.
3. Banners- fitment, replacement or repair (without sewing)
4. Melting link (temperature flag) - replacement

## Slide 15: E) INSTRUMENTS AND EQUIPMENT (HAB, GB, HAA)
Batteries-replacement for self contained instruments and communication equipment.
Communication, navigation devices, instruments and/or equipment – Remove and replace self contained, instrument panel mounted communication devices with quick disconnect connectors

## Slide 16: NPA FCL: Flight Crew Licensing
ICAO PPL (Full ICAO compliance)
Light Aircraft Pilot Licence (LAPL)
Balloon = LAPL(B) Publication in April 2008. Comments accepted until June.
HÅ 2008-03-30

## Slide 17: General Proposals
Age 16 years old to hold the LAPL and age 14 to start training & 1st Solo
Not for remuneration in non-commercial operations
VFR Day (subject to a night qualification)
Licence valid for life and the privileges subject to:
  Valid medical
  Within 24 months, have experience relevant to Category, OR
  Within 24 months, have reduced experience but training flight with instructor, OR
  Check with an instructor
Medical by GP or House doctor

## Slide 18: 1. Size Restrictions. LAPL(B)
Hot air balloons/airships: 4,000 m3
Gas balloons: 1200 m3
max 3 passengers, never more than 4 POB
HÅ 2008-03-30
Balloon Proposals. LAPL(B)

## Slide 19: 2. Training criteria
At least 16 hours dual instruction including 1 supervised solo flight of 30 minutes, minimum 8 launches & ascents
Conversion to another Class Rating
LAPL(B) Classes: Hot Air, Hot Air Airship, Gas balloons

## Slide 20: Ratings
Night flying
LAFI (B) Light Aircraft Flight Instructor
  Minimum 75 hours balloon flight time
  30 hour theoretical knowledge and instruction techniques
  Minimum 3 hours dual flight instruction
LAFE (B) Light Aircraft Flight Examiner

## Slide 21: AMC (Acceptable means of Compliance)
Practical training syllabus
LAFI training course
Skill test
Medical form

## Slide 22: NPA OPS: (OPERATIONAL REGULATIONS)
General Operating and Flight Rules
SUBPART A Pilot-in-command responsibilities
SUBPART B Flight preparation and operation
SUBPART C Aircraft performance and operating limitations
SUBPART D Instruments, Data and Equipment
SUBPART E Communication and navigation equipment
SUBPART F Manuals, Logs and Records

## Slide 23: (ADVANCE) NOTICE of PROPOSED AMENDMENTS
A-NPA 14-2006 June-October 2006
NPA 2007-08. Part M & Pilot / owner maintenance 22 June - 15 Oct. 2007
NPA-FCL March - June 2008
NPA-ELA. Initial airworthiness March - June 2008
NPA-OPS May/June - Aug/Sep 2008